## Slide 1: TLEP: a first step on a long vision for HEP
M. Koratzinos
On behalf of the TLEP steering group
Chios, 27 April 2013

## Slide 3: You have heard it here first!

## Slide 4: Scientific Motivation for TLEP (1)
A new boson with mass ~ 126 GeV, and with SMS properties
  Example : H(126) → ZZ → 4 leptons in CMS and ATLAS
    H(126) couples to the Z boson : important for e+e- colliders!
      gHZZ compatible with SM prediction (within ±30%)
      Scalar hypothesis favoured
      mH known to ~ 400 MeV
      sHZ largest at √s = 250 GeV
Moriond EW ’13

## Slide 5: Scientific Motivation for TLEP (2)
The discovered Higgs boson is indeed (very) Standard
  A summary of all available data so far :
  A sign that New Physics might not be around the corner
    As it would modify the Higgs branching fractions (How much ? See in a few slides.)
      Need to measure more precisely (How precisely ? See in a few slides.)
J. Ellis et al.
Global fit
Red line = SM, dashed line = best fit

## Slide 6: Higgs measurements
Precision needed for Higgs measurements ?
  Does H(126)
    Couple to fermions ?
    Account for fermion masses ?
    Fully account for EWSB ?
    Has SM coupling to gauge bosons ?
    Decay to new, visible, particles ?
    Decay to invisible particles ?
    Have the “proper” mass and width ?
    Show any sign of new physics ?
  What is the precision needed to answer all these questions in a useful manner ?
    We attempt to answer in the next slide
57.9 ± 1.7 %
21.6 ± 0.6 %
8.2 ± 0.8 %
6.4 ± 0.4 %
2.8 ± 0.3 %
2.6 ± 0.1 %
0.27 ± 0.02 %
PJ and G. Ganis
S. Dittmaier et al

## Slide 7: How accurately do we need to measure the Higgs couplings?
Example : Precision for Higgs couplings
  Maximum deviations with respect to SM couplings, as a function of new physics scale
    SUSY , for tanb = 5
    Composite Higgs
    Top partners
    Other models may give up to 5% deviation with respect to the Standard Model
  Maximal deviations for the new physics scale still allowed by LHC results
This strongly influences the strategy for Higgs factory projects
  Need at least a per-cent accuracy on couplings for a 5s “observation”
    And sub-percent precision if new physics is at the (multi-)TeV scale
H. Baer, M. Peskin et al.
J.D. Wells et al.

## Slide 8: SM closure tests
If no new physics is found, what next ?
  Once mH is known, the standard model has nowhere to go !
    Very strong incentive to revisit and improve all precision measurements
      Z pole, WW threshold
      Higgs couplings
      Top quark properties
      Rare decays (Bs → mm, etc.)
    To become sensitive to (multi-)TeV New Physics
→ Programme unique to TLEP
→ Also at the Z pole, unique to TLEP
→ Integrated luminosity unique to TLEP
R. Kogler et al.
LHCb 2013

## Slide 9: Precision at the LHC
The LHC *is* a Higgs factory. However, precision does not reach the sub-percent level needed to look for deviations Beyond the SM
Approved LHC, 300 fb-1 at 14 TeV :
  Higgs mass at 100 MeV
  Disentangle Spin 0 vs Spin 2 and main CP component in gg/ZZ*
  Coupling precision / Experiment
    ZZ, WW, 5-6%
    bb, tt 10-15%
    tt, mm 3-2 s effect
    gg , gg 5-11%
HL-LHC, 3000 fb-1 at 14 TeV:
  Higgs mass at 50 MeV
  More precise studies of Higgs CP sector
  Coupling precision / Experiment
    ZZ, ZW, 1-5%
    bb, tt, tt, mm 3-10%
    gg and gg 2-7%
    HH >3 s (2 Expts)
Assuming sizeable reduction of theory errors
CMS (#177) and ATLAS (#174) contributions to the European Strategy (2012)

## Slide 10: Paths towards the future : Precision Higgs Factories
Several options for Higgs factories are being studied
This talk
(mostly TLEP)
Not encouraged by
European Strategy
Smaller Physics
Potential
Studied for decades
e+e- colliders have largest potential
as Precision Higgs Factories

## Slide 11: A circular machine?
LEP2 reached the HZ production threshold to within 15%...
…so nature has given us a gift with the light Higgs: the next Higgs factory does not necessarily need to be a linear!
Therefore we can take advantage of the progress in circular machines since the time of LEP, and we can come up with a machine with much higher luminosity
Crucially, this luminosity is higher than what can be achieved at linear machines, and a circular machine has the potential for multiple interaction points…
…but it is not (per ce) upgradable in energy, with a ‘brick wall’ reached above around 350GeV

## Slide 12: Challenges (accelerator)
Can high luminosity be achieved?
Is the synchrotron radiation (that increases fast with energy) manageable?
Can an RF system be built to supply the energy lost in SR?
Can the power consumption of such a machine be reasonable?
Are there any showstoppers regarding achieving the above goals? (beamstrahlung)

## Slide 13: Luminosity
It turns out that luminosity is a function of
  Macroscopic parameters:
    bending radius
    power consumption
    Beam energy
  Accelerator parameters:
    Beta*_y (and longitidinal beam size)
    Vertical beam-beam parameter
…while respecting beamstrahlung limits

## Slide 14: Luminosity
The luminosity of a circular collider is
constants
Total SR power
Beam energy
Bending radius
Beam-beam parameter (=0.03 to 0.15)
~1mm
~0.7

## Slide 15: Maximum luminosity
…for a given energy, tunnel radius and power dissipation, effectively depends on what kind of a beam-beam parameter we can reach (the beam-beam limit).
Extrapolating from LEP we get the following (together with the expected luminosities for the ILC and CLIC):
Chart: max. luminosity × number of IPs
| 90 | 110 | 160 | 200 | 240 | 300 | 350 | 360
TLEP 2 IPs | 7.1719e+35 | 4.9976e+35 | 2.546e+35 | 1.7038e+35 | 1.2271e+35 | 8.2121e+34 | 6.2223e+34 | 5.9146e+34
TLEP 3 IPs | 9.1472e+35 | 6.3741e+35 | 3.2472e+35 | 2.1731e+35 | 1.5651e+35 | 1.0474e+35 | 7.936e+34 | 7.5437e+34
TLEP 4 IPs | 1.0871e+36 | 7.575e+35 | 3.859e+35 | 2.5825e+35 | 1.86e+35 | 1.2447e+35 | 9.4312e+34 | 8.9649e+34
ILC | 3e+33 | 5e+33 | 8e+33 | 1.3e+34 | 1.9e+34 | 5e+34
CLIC | 2.3e+34 | 2.9e+34 | 3.3e+34 | 5e+34
TLEP:
ρ = 9000km
PSR = 100MW
Caveat: provided no Beamstrahlung limitations
My own extrapolation – not endorsed by TLEP
TLEP
ILC
CLIC

## Slide 16: Beamstrahlung
Beamstrahlung is the effect of an incoming electron radiating a hard photon in the presence of the electric field of the opposing beam. In circular colliders this might affect beam lifetimes. In linear colliders it smears the beam energy.
If the number of photons above the momentum acceptance of the machine radiated in every collision is high, the beam lifetime suffers
M. Zanetti
The effect of beamstrahlung is very strong in linear colliders and it results in smearing the beam energy
M. Zanetti
Momentum acceptance

## Slide 17: Beamstrahlung mitigation
The mitigation possibilities against low lifetimes due to beamstrahlung are:
  High momentum acceptance
  Very flat beams (high ratio of horizontal to vertical emittance)
  High top-up rate
  Charge compensation

## Slide 18: RF issues
TLEP energy loss per turn @ 175GeV: 9GeV
Choice of frequency: 700-800MHz
Choice of accelerating gradient: 20MV/m dictated by efficiency (up to 35MV/m possible)
Total length of RF system: 900m (LEP2 850m)
Total accelerating power: 12GV (@175GeV)
Working on a preliminary power estimate
BNL 5-cell 700 MHz cavity
 | TLEP 120 | TLEP 175
RF systems | 173-185 MW | 
cryogenics | 34 MW | 
top-up ring | 3 MW | 5 MW
Total RF | ~220 MW | ~220 MW
Preliminary power consumption RF system

## Slide 19: What size for a circular collider?
Luminosity:
  There is a relationship between luminosity and bending radius – so the bigger the better
  (this relationship is not so straightforward due to the interplay between radius and beam-beam limit)
Energy reach:
  Here size really matters
    A 80km ring can reach the ttbar threshold of 350GeV
    A 27km ring can reach the ZH threshold at 240GeV
Our strategy:
  Aim for TLEP in a new tunnel which will later house a very high energy pp collider
  LEP3 is a backup in case of severe financial limitations

## Slide 20: TLEP : a unique Higgs Factory … and much more !
PSB
PS (0.6 km)
SPS (6.9 km)
LHC (26.7 km)
TLEP : e+e-, up to
√s ~350 GeV
VHE-LHC : pp,
√s ~ 100 TeV
LEP3 : e+e-, up to
√s ~ 240 GeV
HE-LHC (33 TeV)
(CERN implementation)
F. Zimmermann
(9 GeV lost per turn)
With a new 80-100 km circular tunnel :
  TLEP Physics case : Precision measurements sensitive to multi-TeV New Physics
    TeraZ (√s~mZ), MegaW (√s~2mW), Higgs Factory (√s~240 GeV), top (√s~350 GeV)
      With luminosity 20-1000 × larger than projects of similar timescale and cost
  Followed by VHE-LHC : Direct search for New Physics in the 10-100 TeV range
    √s ~ 100 TeV (with 20T magnets)
      Also allows the HHH coupling to be measured to a few %

## Slide 21
«Pre-Feasibility Study for an 80-km tunnel at CERN»
John Osborne and Caroline Waaijer,
CERN, ARUP & GADZ, submitted to ESPG
80-km tunnel in Geneva area – “best” option
even better
100 km?

## Slide 22: Beam lifetime at TLEP
At these luminosities, beam lifetime ~ 15 minutes (Bhabha scattering)
  Solution : double ring and continuous top-up injection, as at PEP-II
    Note : Soon to be realized at Super-KEKB, beam lifetime ~ 5 minutes
        Top-up injection : Schematic cycle
        (Provisional logo)
        Contest to be organized !
A. Blondel
TLEP
F. Zimmermann
M. Koratzinos

## Slide 23: Power consumption
TLEP would consume a bit more than the current contract of CERN with EdF (200MW), but would produce more Higgs particles per watt than any other similar project
Power consumption | TLEP 175
RF including cryo | 230MW
cooling | ~5MW
ventilation | 27MW
Magnet system | 14MW
experiments | 25MW
General services | 15MW
Polariz. wigglers | –
Total | ~320MW
Very preliminary

## Slide 24: TLEP Physics case as a Higgs Factory
Summary of the ICFA Higgs Factory Workshop (FNAL, Nov. 2012)
Best
precision

## Slide 25: TLEP physics case as a Higgs factory
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      ILC250 would complement LHC (esp. for GH , Ginv , gHcc , gHbb)

## Slide 26: TLEP physics case as a Higgs factory
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      ILC250/350 would further complement LHC, but does not cover the physics case

## Slide 27: TLEP physics case as a Higgs factory
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      LEP3 would be an advantageous back-up : larger lumi, several IPs, smaller cost

## Slide 28: TLEP physics case as a Higgs factory
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      TLEP would be a superior option (see zoom next page)
See zoom
Next page

## Slide 29: TLEP physics case as a Higgs factory
Same assumptions as for HL-LHC for a sound comparison
  Total width fixed to the sum of the visible partial widths + correction (Dg/g ~ 1/2 DBR/BR)
      TLEP : sub-percent precision, needed for (multi)-TeV New Physics sensitivity

## Slide 30: Cost
It is clear that for such a project in its infancy, no cost estimate exists
This does not prevent one of us (P. Janot) to come up with his own very preliminary estimate which should be taken with a grain of salt.

## Slide 31: Cost per Higgs – by Patrick Janot
LEP3 : A cost-effective option
  Tunnel : 0 $ - Cryoplant : 0$
  Two detectors : 0$ - Four detectors : 1 G$ Total : 1 – 2 G$
  RF + Magnets + Injector Ring : 1 G$
  100,000 Higgs boson / detector / 5 years @ 240 GeV : 5 k$ / Higgs boson
TLEP : A long-term vision
  Tunnel : 4 G$
  Four detectors : 2 G$ Total : 9 G$
  RF + Cryo + Magnet + Injector Ring : 3 G$
  500,000 Higgs boson / detector / 5 years @ 240 GeV : < 4.5 k$ / Higgs boson
Comparison with ILC
  Total Cost : > 10 G$
  70,000 Higgs boson / 5 years @ 240 GeV
of which 5 G$ in common
with SHE-LHC
> 150 k$ / Higgs boson

## Slide 32: Top Measurements at √s ~ 350 GeV
Measurement of mtop perhaps more important than originally thought
Meta-stability favoured at 2s : need to know mtop from e+e-
→
→
Strumia et al, Moriond EW ‘13

## Slide 33: Smaller √s : Impact of TeraZ and MegaW
Revisit and improve the LEP precision measurements
  TLEP can do the entire LEP1 physics programme in 5 minutes (Detector calibration !)
  Important : Polarization up to the WW threshold with TLEP
    Very precise beam energy determination (10 keV) : unique to circular colliders
      Measure mZ, GZ to < 0.1 MeV, mW to < 1 MeV, sin2θW to 2.10-6 from ALR
 | LEP | ILC | LEP3 | TLEP
√s ~ mZ | MegaZ | GigaZ | ~TeraZ | TeraZ
Lumi (cm-2s-1) #Z / year Polarization vs LEP1 | Few 1031 2x107 no 1 | Few 1033 Few 109 easy ~5-10 | Few 1035 Few 1011 yes (T, L) ~50 | 1036 1012 yes (T,L) ~100
√s ~ 2mW |  |  |  | 
Lumi (cm-2s-1) Lumi / IP / year Error on mW | Few 1031 10 pb-1 220 MeV | Few 1033 50 fb-1 7 MeV | 5x1034 500 fb-1 o.7 MeV | 2.5x1035 2.5 ab-1 0.4 MeV
√s ~ 200-250 GeV |  |  |  | 
Lumi (cm-2s-1) Lumi / IP / 5 years Error on mW | 1032 500 pb-1 33 MeV | 5x1033 250 fb-1 3 MeV | 1034 500 fb-1 1 MeV | 5x1034 2.5 ab-1 0.4 MeV
Asymmetries, Lineshape
WW threshold

## Slide 34: Smaller √s : Impact of TeraZ and MegaW
Case 1 : Only SM physics in EW Radiative Corrections – Stringent SM Closure test
  Set stringent limits on weakly interacting new physics (mH, mW and mtop known)
    Much theoretical work also needed
Case 2 : Some weakly interacting new physics in the loops ?
  Will cause inconsistency between the various observables
    Become sensitive to multi-TeV WINP
      LEP1 was sensitive to ~ 200 GeV (mtop)
+
mW
?
Linear
(ILC)
Circular
(LEP3)
mH = 126 GeV
Circular
(TLEP)
M. Grunewald

## Slide 35: Experimental challenges
Experimental challenges are numerous : TLEP(Z)
  At TLEP(Z), the hadronic Z event rate will be 30 kHz
    Same rate of bunch crossings as at LHC (40 MHz)
    CMS current high-level trigger rate is about 1 kHz
      (But hadronic Z events typically 20 times smaller than typical LHC event)
    Need to design a detector and a DAQ system able to cope with these rates
      A clever mixture of LHC detector (rate) and ILC detector (precision)
        Need to study what is the precision needed for each sub-detectors
        Is a CMS-like detector sufficient ? (~OK for Higgs studies)
  Small angle Bhabha event rate (lumi measurement) will be even larger : 120 kHz
    Essential to measure cross sections, hence the Z lineshape (mZ, Gz)
      Negligible beamstrahlung is a great advantage
        No background in the luminometers
        Energy spectrum perfectly known (hence Bhabha cross section)
      Will need theoretical developments to understand se+e- to better than 5 x 10-5
  Limiting uncertainties on aQED(mZ) and as(mZ) must be overcome
    Possible with the billions of e+e- → e+e-(g) , m+m-(g) and qq(g) events ?
      Will affect all Z peak asymmetries, and mZ vs mW interpretation
-
P Janot, A. Blondel
Nn

## Slide 36: Detectors for TLEP and LEP3
For LEP3, obvious detectors are CMS and ATLAS
  CMS demonstrated to be adequate with today’s design + upgraded pixel detector
    Phase 2 upgrades : LEP3 could be seen as an alternative to HL-LHC
    Tunnel By-passes need to be dug out for the accelerating ring
For TLEP, new detectors are in order (used CMS for Higgs studies in this talk)
  Holistic approach: design caverns and detectors to be re-used in pp collisions (as new)
    TeraZ sets the scale for DAQ (2600 bunches) + forward EM calorimetry (lumi)
    TLEP(H) sets the scale for precision (tracker, ECAL, particle flow, b tagging)
    SHE-LHC sets the scale for magnetic field, calorimeter depths, tracker pT reach
      Could envision a staged approach
E. Meschi
From TLEP…
…to VHE-LHC

## Slide 37: Possible Timescales
Similar timescales for TLEP and LEP3
TLEP
  Design study : 2013-2017
  Next European Strategy Workshop : 2017-2018
  Decision to go and start digging : 2018-2019
  Start installation in parallel with HL-LHC running : 2023 - …
  Start running at the end of HL-LHC running : 2030 - …
LEP3
  Design study : 2013-2017 (spin-off of TLEP design study)
  Next European Strategy Workshop : 2017-2018
  Decision to go : 2018-2019
  Start installation at the end of LHC running : 2022 - …
    Tunnel probably irradiated at the end of HL-LHC
      LEP3 is an alternative of HL-LHC, and could be followed by HE-LHC in 2040
  Start running when ready : 2027 - …
 | 2010 |  |  |  |  |  | 2015 |  |  |  |  | 2020 |  |  |  |  | 2025 |  |  |  |  | 2030 |  |  |  |  | 2035 |  |  |  |  | 2040
LHC |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HL-LHC | R&D + constr |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TLEP* |  |  |  | Design + R&D + construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
VHE-LHC* | Design + R&D + construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 38: European strategy
Recommendations from European Strategy Group
  High-priority large-scale scientific activities
    Recommendation #2
    Excerpt from the CERN Council deliberation document (22-Mar-2013)
d) To stay at the forefront of particle physics, Europe needs to be in a position to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update, when physics results from the LHC running at 14 TeV will be available.
CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.
The two most promising lines of development towards the new high energy frontier after the LHC are proton-proton and electron-positron colliders. Focused design studies are required in both fields, together with vigorous accelerator R&D supported by adequate resources and driven by collaborations involving CERN and national institutes, universities and laboratories worldwide. The Compact Linear Collider (CLIC) is an electron-positron
machine based on a novel two-beam acceleration technique, which could, in stages, reach a centre-of-mass energy up to 3 TeV. A Conceptual Design Report for CLIC has already been prepared. Possible proton-proton machines of higher energy than the LHC include HE-LHC, roughly doubling the centre-of-mass energy in the present tunnel, and V-LHC, aimed at reaching up to 100 TeV in a new circular 80km tunnel. A large tunnel such as this could also host a circular electron-positron machine (TLEP) reaching energies up to 350 GeV with high luminosity.

## Slide 39: Design Study : 2013 – 2018

## Slide 40: Who are we?
TLEP Steering group (ad interim)
  Roy Aleksan
  Alain Blondel
  John Ellis
  Patrick Janot
  Mike Koratzinos
  Marco Zanetti
  Frank Zimmermann

## Slide 41: Conclusions
TLEP is a unique project for Europe and the HEP community
It offers the best performance compared to similar cost and timescale projects
LEP3 offers an excellent backup plan
It is upgradable to a very high energy pp collider (~100TeV)
The design study effort has just started: it is an exciting project with short delivery times (2018)
We need to wait for the LHC 14TeV run, but there is a high chance that TLEP/VHE-LHC will be the best way to go for the next 50 years

## Slide 42: Join us!
You can contribute to the design study by filling the form
  http://tlep.web.cern.ch/contribute-to-the-design-study
  …indicating in which field you would like to contribute
  (no MoU currently, institution board to be assembled)
Kick-off meeting (at CERN) expected end of the year/beginning of 2014
Currently 174 expressions of interest – only 5 Greeks